## Slide 1: Patient-specific Optimization of a Neurosurgical Robotic Manipulator
Michael Brauckmann – Daniel Miller 4/29/14

## Slide 2: Overview
Problem Description
Genetic Simulation Overview
Robot Description
  Parameterization of Linkage
Forward and Inverse Kinematics
Linkage Evaluation
  Fitness Function
  Collision Detection
Results
Future Work

## Slide 3: Problem Description
Optimize the robot’s geometry
  To the patient’s dimensions
  To the surgical site
  To the surgical workspace
Avoid collisions
  Patient & MRI Machine
Other possible subtasks
  Maximize clearance
  Maximize rigidity
  …
The AIM Lab RCM Robotic Manipulator

## Slide 4: Problem Description
Optimize the robot’s geometry
  To the patient’s dimensions
  To the surgical site
  To the surgical workspace
Avoid collisions
  Patient & MRI Machine
Other possible subtasks
  Maximize clearance
  Maximize rigidity
  …
The AIM Lab RCM Robotic Manipulator

## Slide 5: Genetic Simulation Overview
Motivation
Complex non-linear parameter space
  Small change in linkage dimension may result in inadmissible configuration (i.e Collision)
No quantitate way to compare configurations (yet.)
Genetic Algorithms
Generate a “population” of varying linkages
Evaluate each linkage against a particular task
  Weight performance in different categories
Select high-performing individuals
  Proportional to performance
Mutate members of population
  Crossover
  Random mutation
Repeat

## Slide 6: Robot Description
3 Rotational & 4 Translational joints
Linkage rotates about point relative to base
Linkage Parameters:
  Link 1 – Length
  Link 1 - Radius
  Link 2 – Length
  Link 2 – Radius

## Slide 7: Forward and Inverse Kinematics
Forward Kinematics
Kinematics determined by with Denavit-Hartenburg parameters
Resulting linkage motions rotate about a fixed point
Location of fixed point determined by location of XYZ Table

## Slide 8: Forward and Inverse Kinematics
Inverse Kinematics
Given the point of entry a geometrical solution is easy
The two angles are defined by the 3D slope of the line from entry point to goal
The XYZ Table must Lie on a parallel Line
This line can be parameterized by the needle extension to give an exact point

## Slide 9: Linkage Evaluation Fitness Function
Test Parameters
Percentage of IK solutions that collided
Percentage of Workspace with at least one none colliding solution
Percentage of IK solutions not in bounds of XYZ table
Other Possibilities
One over the total Link Length
  Short links are stiffer and more accurate
Median extension of needle
  keeping it near middle of range tend to increase distance from collision
Average distance of a point to nearest obstacle
  Good for collision avoidance

## Slide 10: Linkage Evaluation Collision Detection
Collisions approximated with shape primitives
  Shape collision trivial to calculate
  Concave Mesh collision very difficult to calculate
Collision with patient
  Approximated as set of Spheres
Collision with MRI bore
  Approximated as Cylinder

## Slide 11: Linkage Evaluation Collision Detection
Collisions approximated with shape primitives
  Shape collision trivial to calculate
  Concave Mesh collision very difficult to calculate
Collision with patient
  Approximated as set of Spheres
Collision with MRI bore
  Approximated as Cylinder

## Slide 12: Results!
Successfully generated viable linkages through genetic simulation
Created a fast collision detection approximation
Resolved redundancy in manipulator

## Slide 13: Results!
Successfully generated viable linkages through genetic simulation
Created a fast collision detection approximation
Resolved redundancy in manipulator

## Slide 14: Results!

## Slide 15: Thank you! Any questions?